Suggested EIPS Test Protocol for a

1200x1000mm, Rackable, Full 4 way entry Pallet

for International Use

I.   Physical Properties

Pallet Size							1200x1000mm

Top deck coverage 					60% minimum

Bottom deck coverage 					35% minimum

Vertical clearance under top deck			95 mm minimum

156 mm maximum

Horizontal clearance

Maximum width of center posts or stringers	160 mm (6.3 in.)

Minimum width between outer posts or stringers	720 mm (28.3 in.)

Maximum height 					165 mm (6.5 in.)

Maximum weight					22 kg (50 lbs.)

Fasteners, if needed, should conform to the minimum quality guidelines in ASME MH1, Part 3.

# II.    Racking Performance

Must safely support a 1000-pound load when racked across the length and racked across the width, according to the procedures outlined in ASTM D1185. The suggested load is corrugated boxes, 6 boxes per layer, 5 layers high. Pallet deflection should not exceed 0.50 inches with this load after the required test period.

III.    Stacking Performance

Must safely support a 1000-pound load per pallet when stacked up to 3 loaded pallets high, according to the procedures outlined in ASTM D1185. The suggested load is corrugated boxes, 6 boxes per layer, 5 layers high. Deck deflection should not exceed 0.25 inches with this load after the required test period.

IV.  Conveyor  Performance

Must safely support a 1000-pound load when supported across the length and across the width on chain conveyors located midway between the posts or stringers, according to the procedures outlined in ASTM D1185. The suggested load is corrugated boxes, 6 boxes per layer, 5 layers high. Pallet bottom deck deflection should not exceed 0.25 inches with this load after the required test period.

V.   Coefficient of Friction

The minimum suggested Static COF is 0.40, as measured on the following 4 pallet surfaces: Top Deck with corrugated boxes, Underneath top deck on steel forktines, Bottom deck on steel surface, and empty Pallet on empty Pallet (stacked).

VI.  Relative Durability

Level I  (one way pallets)

Corner Drop: 					3 drops from 40” height

Tine Tip Impacts on Block or Stringer Ends 	3 impacts at 6 inches

Tine Heel Impacts on Lead Edges			3 impacts at 24 inches

Level II  (returnable pallets)

Corner Drop: 					6 drops from 40” height

Tine Tip Impacts on Block or Stringer Ends 	3 impacts at 12 inches

Tine Heel Impacts on Lead Edges			3 impacts at 48 inches

Pallets tested for durability according to the procedures outlined in ASTM D1185. Suggested load is 1000 pounds of deadload (corrugated boxes not necessary). Pallets should pass each level without structural damage or more than 1.5% diagonal deformation.